Cummins Insite Inline5 Inline6 Comparison

| Can ECU Flash before 1st.Jan.2015 Cummins engine According the original Inline6 chip 1:1 to design appearance, all chips welded, protective in good, fully functional, include canbus2 design. Inline5 cut corners to save costs, NEXIQ USB link also not have canbus2 |
| --- |
| CPU: DSP56F807PY80E | CPU: MCF5272CM66J Freescale car chip | MCF5253VM140 Freescale car chip |
| CPU model to determine the speed of diagnosis when flash, finished in 5 minutes, or you want to wait for 10 minutes? |
| Frequency：80MHz core frequency | Frequency： 66MHz | Frequency：140MHz |
| RAM:128k | RAM:256k | RAM：512k |
| 16 bit | 32 bit | 32 bit |
| Wire：9pin，6pin，obd，Circle:OBD16 | Wire：9pin，6pin，obd，Femal:3pin | Wire：9pin，obd，Femal:3pin，Mail:3pin，2pin |
| Optional cable： | Optional cable： | Optional cable：6pin，circle:16pin |
| Insite7.5 No need to change time of computer when install | Insite7.5 No need to change time computer | Insite7.5 No need to change time pf computer |
| Insite7.6.0 need to change the time of computer to install | Insite7.6.0 need to change the time of computer to install | Insite7.6.2 need to change the time of computer to install |
| No calibration disc | No calibration disc | Free of charge a value $50 incal2014 calibration ECU flash for VIP customer. |
| Windowsxp/7/8 32bit/64bit Calibration not support 64 bit computer | Windowsxp/7/8 32bit/64bit Calibration not support 64 bit computer | Windowsxp7/8/10 32bit/64bit Calibration not support 64 bit computer |